## Slide 1: TBO – Implementation at MUAC
TBO Symposium 04-06 June 2024
Peter Hendrickx
Head ATM Development

## Slide 2: Datalink Implementation at MUAC
i4D under SESAR1
ATS B2/ADS-C under SESAR2020
Fully Operational
PRE-OPS
CP1 Target
2009-2016
2016-2022
Continuous Evolutions
2012:
1st Flight Trial
2014:
2nd Flight Trial
July
2019
May
2022
Tool enhancements
HMI enhancements
Main pilar for TBO
Updates of Standards
CPDLC Fully Operational
CPDLC v2
July
2019
CPDLC v1
2001
December 2027
All as evolutions, in small steps!

## Slide 3: ATS-B2 MUAC
DISPLAY OF EPP (a/c intent trajectory up to 128 waypoints)
ADS-C
TOC
DISPLAY OF TOC & TOD
DISPLAY TOA RANGE (Time Of Arrival)
EPP route
FDPS route
Earliest time at point
Latest time at point
TOD
Discrepancy Indication

## Slide 4: ATS-B2 MUAC
DISPLAY OF EPP (a/c intent trajectory up to 128 waypoints)
Safety Improvement / Workload Reduction
TOC
DISPLAY OF TOC & TOD
DISPLAY TOA RANGE (Time Of Arrival)
EPP route
FDPS route
Earliest time at point
Latest time at point
TOD
Discrepancy Indication
Safety Improvement
Reduction ATCO Mental Workload

## Slide 5: ATS-B2 MUAC
Efficiency improvement
DISPLAY OF EPP (a/c intent trajectory up to 128 waypoints)
TOC
DISPLAY OF TOC & TOD
DISPLAY TOA RANGE (Time Over Arrival)
EPP route
FDPS route
Earliest time at point
Latest time at point
TOD
More “when ready”
Totals 15/11/2022-31/11/2023
Descend at ToD vs. 1500 fpm profile
22.205 nm maintaining
17.764 kg fuel saved
56.134 kg CO2 saved
Note: fuel/CO2 values are dependent on cost index/gross weight.

## Slide 6: ATS-B2 MUAC
DISPLAY OF EPP (a/c intent trajectory up to 128 waypoints)
TOC
DISPLAY OF TOC & TOD
DISPLAY TOA RANGE (Time Over Arrival)
EPP route
FDPS route
Earliest time at point
Latest time at point
TOD
Fuel/CO2 savings
Shortcut 5 nm @ FL360
A320: ~25 kg / 79 kg CO2
A330: ~60 kg / 189 kg CO2
Shortcut 20 nm @ FL360
A320: ~100 kg / 316 kg CO2
A330: ~240 kg / 758 kg CO2
Note: values are dependent on cost index/gross weight.
Efficiency improvement

## Slide 7: ATS-B2 MUAC
DISPLAY OF EPP (a/c intent trajectory up to 128 waypoints)
ADS-C with CPDLC V2 – Efficiency Improvement
TOC
DISPLAY OF TOC & TOD
DISPLAY TOA RANGE (Time Over Arrival)
EPP route
FDPS route
Earliest time at point
Latest time at point
TOD

## Slide 8: ATS-B2 benefits
Safety enhancement
Workload reduction
Improving efficiency
Better traffic management
Better prediction of sector loads & runway occupancy times.
More effective traffic management
Enabling capacity increase
Controllers
Network
Future
Improved meteo models
Enhanced Extended AMAN predictions
Enabling automation in ATC -> Capacity increase
Trajectory Based Operations
Airlines
Optimized profiles & routes
Time saving
Fuel saving
CO2 emissions reduction
Pilots
Safety enhancement
Workload reduction
Improving efficiency

## Slide 9: FF-ICE R1 Implementation
Implementation plan 2025 under construction:
  Call for Tender for Industry being prepared
Full eFPL in FIXM Format processed by FDPS targeted 2026-2027
Expected benefits:
  More data available:
    Exact use TBD – depends on quality – TP/Display purposes
  Being prepared for possible other FF-ICE R1 services:
    Consolidated feedback
    Unconstrained Desired Trajectory
  Being prepared for FF-ICE R2:
    Involvement of Local Flow Management in optimisations during execution phase
    Subject of SESAR Network TBO Project

## Slide 10
Thank you!
Peter.hendrickx@eurocontrol.int