## Slide 1
TBO Global Concept
Crystal Kim, ICAO
Henk Hof, EUROCONTROL
ATMRPP

## Slide 2: Global Air Traffic Management Operational Concept (Doc 9854)
1st Edition in 2005
CDM/ATFM
FF-ICE
SWIM
TBO
Connected Aircraft
Detailed concepts & performance framework
SARPs, PANS, and Guidance material
The Foundation
ATM System Requirements
Global Air Navigation System Performance

## Slide 3: Global Air Traffic Management Operational Concept (Doc 9854)
The Foundation
considers the trajectory of a manned or unmanned vehicle during all phases of flight …
manages the interaction of that trajectory with other trajectories or hazards to achieve the optimum system outcome, with minimal deviation from the user-requested flight trajectory, whenever possible.
individual aircraft performance, flight conditions, and available ATM resources will allow dynamically optimized 4-D trajectory planning.
Management by trajectory does not mean that every aspect of a flight, including arrival profile, runway, taxi path and gate needs to be predetermined and captured in detail in the agreement at the time of departure. The agreement and the management of that agreement will have the details required by the traffic management phases that the flight is subject to at the time the initial agreement and subsequent updates are made.
And many more….

## Slide 4
Global TBO Concept
Broad support from the 13th Air Navigation Conference (Montréal, 9-19 October 2018)
Integrated in the Global Air Navigation Plan and Aviation System Block Upgrade Framework

## Slide 5
Needs of Airspace Users

## Slide 6: Trajectory revision on AU initiative due to Weather conditions changes
Flight efficiency
through Flight Planning

## Slide 7: Collaboration – Today
FOC Automation
Flight Deck Automation
ATC Automation
TFM Automation
Limited In-Flight Coordination
Plan not followed
Imprecise execution
Automation not Informed
Disparate Plans in Automation

## Slide 8: Collaboration – Full TBO Environment
Shared plans, consistent trajectories
FOC Automation
Flight Deck Automation
ATC Automation
TFM Automation
Negotiated Trajectory
Improved Control Precision
Closed Trajectory
Accurate Execution
Automation Informed
Trajectory Constraints
Robust Solutions

## Slide 9
SHARING
Flight/Flow Information
for a Collaborative Environment
(FF-ICE)
MAINTAINING
USING
Trajectory Based Operations
Connected Aircraft

## Slide 10
TBO bringing it all together
Years
Months
Minutes
Days
Hours
Depart
In Flight
Long-term Planning
Mid-term Planning
Tactical Planning
Execution
Capacity Management
Flow Management
Scheduling
Flight Planning
Separation Provision
Traffic Synchronisation
Re-optimisation
ATFM
ATC
AM
AU
AM Airspace Management
ATFM Air Traffic Flow Management
AU Airspace User
ATC Air Traffic Control
AO Aerodrome Operator
Departure AO
Arrival AO
Collaboration
A0
Flight Information

## Slide 11: Framework
Changing Circumstances
Re-optimize
Tactical Interventions
Negotiation
Manage Agreed Trajectory
Deliver Clearance
Maintain
Feedback to AU
Problem evaluation
Keep up with uncertainty & clearances
Share and ensure agreement reflects what has happened
ATC delivers the Agreed Trajectory using clearances
Flight Information Sharing
Legend

## Slide 12: Incorporation of ATFM
Agreed trajectory managed for many flights
Demand Estimation
ATFM Uses Agreed Trajectories for Demand Estimation
Changing Circumstances
ATFM
Capacity Estimation
Capacities for ATFM also changing
Monitor Flow, D&C
Flight Information Sharing
Legend
Flow Information Sharing
Initiate / modify ATFM solutions
Evaluate alternative ATFM solutions
Is there a problem?
Did one go away?
What changes make sense?
Flow data affects flight data
Flow
Flight

## Slide 13: TBO Enablers
Capability | ADS-B | ADS-C | CPDLC | PBN | PBC | PBS | FMS | Connected Aircraft | FF-ICE | SWIM
Pre-Departure Trajectory Negotiation |  |  |  |  |  |  |  |  |  | 
Post-Departure Trajectory Negotiation |  |  |  |  |  |  |  |  |  | 
Trajectory Parameter Exchange |  |  |  |  |  |  |  |  |  | 
TBO Clearances |  |  |  |  |  |  |  |  |  | 
Sharing of Aircraft–Derived Trajectory (ADS-C) |  |  |  |  |  |  |  |  |  | 
Sharing of Aircraft-Derived Trajectory (A/G SWIM) |  |  |  |  |  |  |  |  |  | 
Precise Clearance Execution |  |  |  |  |  |  |  |  |  | 
GATMOC Component Integration |  |  |  |  |  |  |  |  |  | 
ASP Coordination & Negotiation |  |  |  |  |  |  |  |  |  | 
+ Trajectory Prediction Accuracy |  |  |  |  |  |  |  |  |  | 
Legend
 Required
↑ Improves

## Slide 14: TBO Capability Evolution
Airspace User
FPL
Pre-departure Negotiation
Post-departure Negotiation
FOC
FD
Trajectory Accuracy
ADS-B
Shared Parameters
FOC
EFB
Aircraft-Derived
Aircraft 4DT (EPP)
ADS-C
Open Closed
Piecewise End-to-end
Precision where needed
Deliver Agreed
Clearances
Voice
Initial CPDLC
Precise Clearances
ATM Components
TBO Components
Ground Synchronization
Full TBO Integration
Use Trajectory
Create Clearances
Trajectory Revisions
TM Rules

## Slide 15
Wild-West
Image: Personal photograph
Image: NASA/JPL-Caltech
System is performance-driven
No “Big-Bang”
  Mixed-mode: Individual ANSP deploy capabilities along different timelines
  Mixed Equipage: Aircraft operators as well
Expect mixed-mode, mixed-equipage
Need for Synchronization
  ASBUs define timeline for availability of capabilities
  There will be a need for a “minimum-path”
Mixed-mode & transition (1/2)

## Slide 16
Mixed-mode & transition (2/2)
One size does not fit all
OK to use different pathways and timelines
As long as we all converge interoperably to the same point

## Slide 17: Ongoing TBO work of ICAO (1/2)
1stEdition
Refinement of the concept
Update to GANP

## Slide 18: Ongoing TBO work of ICAO (2/2)
Guidance on the value-driven TBO evolution to support:
  planning and implementation of TBO enablers
  development of proposals for amendment to ICAO provisions as necessary

## Slide 19: Trajectory Based Operations, the Paradigm Change Transformation

## Slide 20
Thank You !