## Slide 1: Automatic Speech Recognition for ATCo Support An application of Artificial Intelligence and its steps from the Idea to Exploratory Research to Industrial Research
Hon. Prof. Dr. Hartmut Helmke,
German Aerospace Center, DLR Project Lead of AcListant®, AcListant®-Strips, PJ.16-04-ASR-W1, MALORCA, HAAWAII

## Slide 2: How many training data is used by Google for training their speech recognizer?
300 hours
3,000 hours
30,000 hours
300,000 hours
3,000,000 hours

## Slide 3: What is Artificial Intelligence?
“Artificial Intelligence is the development of computer systems that are able to perform tasks that would require human intelligence” Schetinin et al. (2018)
In 1940s / 1950s a system multiplying numbers faster than a human was intelligent.
During the 1980s / 1990s: it was chess playing.
Now, we think autonomous cars or zero-person-cockpits are intelligent systems.
Turing-Test

## Slide 4: Application Areas of Artificial Intelligence
Computer Vision
Natural Language
Processing
Automatic
Speech Recognition
Robotics
Planning & Optimization
Expert Systems
Machine Learning
(Deep) Neural Networks
Supervised Learning
Unsupervised Learning
Reinforcement Learning
Behaviour Prediction
DLR Applications with respect to Speech Recognition

## Slide 5: Automatic Speech Recognition & Understanding for Air Traffic Management Applications
Command Prediction
Concept Recognition
THY5KJ REDUCE 160 none OR_GREATER
THY5KJ DESCEND 3000 ft
Voice To Text
hello good morning
turkish five kilo juliet
reduce one sixty or greater
descent three thousand feet
Aircraft: THY5KJ, DLH3ER
Commands:
THY5KJ DESCEND 3000 ft
THY5KJ REDUCE 180 kt …
ATCO
Surveillance Data, Flight Plan Data
Weather Data
TYK5KJ
30
Assistant Based Speech Recognition
Avoid manual input
Reduce ATCo workload
M. Kleinert, H. Helmke, H. Ehr, Chr. Kern, D. Klakow, P. Motlicek, M. Singh, and G. Siol, “Building Blocks of Assistant Based Speech Recognition for Air Traffic Management Applications,” 8th SESAR Innovation Days, Salzburg, Austria, 2018.

## Slide 6: Machine Learning of Speech Recognition Models for Controller Assistance
Radar Data
Voice Recordings
Automatic Learning
Process
Assistant
Based
Speech
Recognition
Group of experts
Assistant
Based
Speech
Recognition
Instead of (highly skilled and paid) experts, machine learning is used.
Dusseldorf
Prague, Vienna
Arthur Samuel (1959):
Machine learning is the field of study that gives computers the ability to learn without being explicitly programmed”
H. Helmke, O. Ohneiser, J. Buxbaum, and C. Kern, “Increasing ATM efficiency with assistant-based speech recognition,” 12th USA/Europe Air Traffic Management Research and Development Seminar (ATM2017), Seattle, Washington, USA, 2017.

## Slide 7: Speech Recognition and Machine Learning Roadmap
2014 2015 … 2018 2019 2020 … 2022
AcListant®-Strips
95%
60 l, Workload Reduction
Prague: 0.6%
Vienna : 3.2%
COTS
Ontology
Tower
Prediction
Pilot, Ops-Room
#97 Remote Tower
Vienna Ops Room
Machine Learning
ASR
SESAR PJ16-04
From Exploratory Research to Industrial Research to the Future in the Ops Room
J. Rataj, H. Helmke, O. Ohneiser: “AcListant® with Continuous Learning: Speech Recognition in Air Traffic Control”
in Lect. Notes Electrical Eng., Vol. 731, (Ed): AIR TRAFFIC MANAGEMENT AND SYSTEMS IV, 978-981-33-4668-0, 488801_1_En (6)

## Slide 8: compared to
Google (US company) uses
300,000 hours of
training data
22 hours of voice recordings from Prague
*

## Slide 9: Thank you very much for your attention

## Slide 10: How many training data is used by Google for training their speech recognizer?
300 hours
3,000 hours
30,000 hours
300,000 hours
3,000,000 hours
Google has used 13,000 times more training data than MALORCA for Vienna resp. Prague
(300,000 versus 22 hours).